## Slide 1
Computer Networking with Mininet

## Slide 2: Introduction to Mininet
Platforms for Network/Systems Teaching
Network Emulator Architecture Mininet: Basic Usage, CLI, API Example Demos: Network Security Conclusion and Questions

## Slide 3: Platforms for Network/Systems Teaching (and Research)
Platform | Advantages | Disadvantages
Hardware Testbed | fast accurate: "ground truth" | expensive shared resource? hard to reconfigure hard to change hard to download
Simulator | inexpensive, flexible detailed (or abstract!) easy to download virtual time (can be "faster" than reality) | may require app changes might not run OS code detail != accuracy may not be "believable" may be slow/non-interactive
Emulator | inexpensive, flexible real code reasonably accurate easy to download fast/interactive usage | slower than hardware experiments may not fit possible inaccuracy from multiplexing

## Slide 4: Introduction to Mininet
Platforms for Network/Systems Teaching Network Emulator Architecture Mininet: Basic Usage, CLI, API
Example Demos: Network Security Conclusion and Questions

## Slide 5: To start with, a Very Simple Network
Host
Switch
Host
firefox
httpd

## Slide 6: Very Simple Network using Full System Virtualization
VM Server
ovs-vswitchd
Linux Kernel
openvswitch kernel module
Host VM
cupsd
Linux Kernel
init
bash
firefox
eth0
tap0
eth0
tap1
Host VM
cupsd
Linux Kernel
init
bash
httpd
eth0
10.0.0.1
10.0.0.2

## Slide 7: Very Simple Network using Lightweight Virtualization
Server (or VM!)
ovs-vswitchd
Linux Kernel
openvswitch kernel module
Network Namespace 1
firefox
veth1
eth0
veth2
Network Namespace 2
httpd
eth0
eth0
10.0.0.1 10.0.0.2

## Slide 8: Mechanism: Network Namespaces and Virtual Ethernet Pairs
Root Namespace
Network Namespace 1
firefox
veth1
eth0
veth2
Network Namespace 2
httpd
eth0
eth0
Software Switch
virtual Ethernet pairs
10.0.0.1 10.0.0.2

## Slide 9: Creating it with Linux
sudo bash
# Create host namespaces ip netns add h1
ip netns add h2 # Create switch
ovs-vsctl add-br s1 # Create links
ip link add h1-eth0 type veth peer name s1-eth1 ip link add h2-eth0 type veth peer name s1-eth2 ip link show
# Move host ports into namespaces ip link set h1-eth0 netns h1
ip link set h2-eth0 netns h2 ip netns exec h1 ip link show ip netns exec h2 ip link show # Connect switch ports to OVS ovs-vsctl add-port s1 s1-eth1 ovs-vsctl add-port s1 s1-eth2 ovs-vsctl show
# Set up OpenFlow controller
ovs-vsctl set-controller s1 tcp:127.0.0.1 ovs-controller ptcp: &
ovs-vsctl show
# Configure network
ip netns exec h1 ifconfig h1-eth0 10.1 ip netns exec h1 ifconfig lo up
ip netns exec h2 ifconfig h2-eth0 10.2 ip netns exec h1 ifconfig lo up ifconfig s1-eth1 up
ifconfig s1-eth2 up # Test network
ip netns exec h1 ping -c1 10.2
s1
h1
10.0.0.1
h2
10.0.0.2
ctrl’er

## Slide 10: Wouldn’t it be great if...
We had a simple command-line tool and/or API that did this for us automatically?
It allowed us to easily create topologies of varying size, up to hundreds of nodes, and run tests on them?
It was already included in Ubuntu?

## Slide 11: Introduction to Mininet
Platforms for Network/Systems Teaching Network Emulator Architecture
Mininet: Basic Usage, CLI, API Example Demos: Network Security Conclusion and Questions

## Slide 12: Mininet command line tool and CLI demo
# mn
# mn --topo tree,depth=3,fanout=3 -- link=tc,bw=10
mininet> xterm h1 h2
h1# wireshark &
h2# python -m SimpleHTTPServer 80 & h1# firefox &
# mn --topo linear,100
# mn --custom custom.py --topo mytopo

## Slide 13: Mininet's Python API
Core of Mininet!! Everything is built on it. Python >> JSON/XML/etc.
Easy and (hopefully) fun
Python is used for orchestration, but emulation is performed by compiled C code (Linux + switches + apps)
api.mininet.org docs.mininet.org Introduction to Mininet

## Slide 14: Mininet API basics
net = Mininet()
# net is a Mininet() object
h1 = net.addHost( 'h1' ) h2 = net.addHost( 'h2' ) s1 = net.addSwitch( 's1' )
# h1 is a Host() object # h2 is a Host()
# s1 is a Switch() object
# c0 is a Controller()
# creates a Link() object
c0 = net.addController( 'c0' ) net.addLink( h1, s1 ) net.addLink( h2, s1 ) net.start()
h2.cmd( 'python -m SimpleHTTPServer 80 &' ) sleep( 2 )
h1.cmd( 'curl', h2.IP() ) CLI( net )
h2.cmd('kill %python') net.stop()
s1
h1
10.0.0.1
h2
10.0.0.2
c0

## Slide 15: Performance modeling in Mininet
# Use performance-modeling link and host classes net = Mininet(link=TCLink, host=CPULimitedHost) # Limit link bandwidth and add delay net.addLink(h2, s1, bw=10, delay='50ms')
# Limit CPU bandwidth net.addHost('h1', cpu=.2)
s1
h1
10.0.0.1
20% of CPU
h2
10.0.0.2
controller
10 Mbps, 50 ms

## Slide 16: Low-level API: Nodes and Links
h1 | = | Host( 'h1' )
h2 | = | Host( 'h2' )
s1 | = | OVSSwitch( 's1', inNamespace=False )
c0 | = | Controller( 'c0', inNamespace=False )
Link( h1, s1 ) Link( h2, s1 ) h1.setIP( '10.1/8' )
h2.setIP( '10.2/8' )
c0.start() s1.start( [ c0 ] )
print h1.cmd( 'ping -c1', h2.IP() ) s1.stop()
c0.stop()

## Slide 17: Mid-level API: Network object
net = Mininet()
h1 = net.addHost( 'h1' ) h2 = net.addHost( 'h2' ) s1 = net.addSwitch( 's1' )
c0 = net.addController( 'c0' ) net.addLink( h1, s1 ) net.addLink( h2, s1 ) net.start()
print h1.cmd( 'ping -c1', h2.IP() ) CLI( net )
net.stop()

## Slide 18: High-level API: Topology templates
class SingleSwitchTopo( Topo ): "Single Switch Topology" def build( self, count=1):
hosts = [ self.addHost( 'h%d' % i )
for i in range( 1, count + 1 ) ] s1 = self.addSwitch( 's1' )
for h in hosts: self.addLink( h, s1 )
net = Mininet( topo=SingleSwitchTopo( 3 ) ) net.start()
CLI( net ) net.stop()
more examples and info available at docs.mininet.org

## Slide 19: Custom Topology Files
# cat custom.py
from mininet.topo import Topo class SingleSwitchTopo( Topo ):
"Single Switch Topology" def build( self, count=1):
hosts = [ self.addHost( 'h%d' % i )
for i in range( 1, count + 1 ) ] s1 = self.addSwitch( 's1' )
for h in hosts: self.addLink( h, s1 )
topos = { 'mytopo': SingleSwitchTopo } # mn --custom custom.py --topo mytopo,3
*** Creating network
*** Adding controller
*** Adding hosts: h1 h2 h3

## Slide 20: Conclusion
Network Emulators can facilitate teaching networking via realistic live demos, interactive labs and course assignments
inexpensive, interactive, real apps and OS, reasonably accurate
downloadable, fast setup
Mininet is a lightweight virtualization/container based emulator
- modest hardware requirements, fast startup, hundreds of nodes
command line tool, CLI, simple Python API
SDN as well as Ethernet/IP networking as well as SD
install using VM, Ubuntu package, or source
mininet.org: Tutorials, walkthroughs, API documentation and examples teaching.mininet.org: Mininet-based course assignments and labs open source: hosted on github, permissive BSD license
Next up: short break, then hands-on lab!