## Slide 1: Introduction to TCP/IP networking

## Slide 2: TCP/IP protocol family
IP : Internet Protocol
  UDP : User Datagram Protocol
    RTP, traceroute
  TCP : Transmission Control Protocol
    HTTP, FTP, ssh

## Slide 3: What is an internet?
A set of interconnected networks
The Internet is the most famous example
Networks can be completely different
  Ethernet, ATM, modem, …
  (TCP/)IP is what links them

## Slide 4: What is an internet? (cont)
Routers are devices on multiple networks that pass traffic between them
Individual networks pass traffic from one router or endpoint to another
TCP/IP hides the details as much as possible

## Slide 5: ISO/OSI Network Model
Seven network “layers”
  Layer 1 : Physical – cables
  Layer 2 : Data Link – ethernet
  Layer 3 : Network – IP
  Layer 4 : Transport – TCP/UDP
  Layer 5 : Session
  Layer 6 : Presentation
  Layer 7 : Application
You don’t need to know the layers just the idea that it is layered

## Slide 6: TCP/IP Network Model
Different view – 4 layers
  Layer 1 : Link
  Layer 2 : Network
  Layer 3 : Transport
  Layer 4 : Application

## Slide 7: OSI and Protocol Stack
OSI: Open Systems Interconnect
OSI Model
TCP/IP Hierarchy
Protocols
7th
Application Layer
6th
Presentation Layer
5th
Session Layer
4th
Transport Layer
3rd
Network Layer
2nd
Link Layer
1st
Physical Layer
Application Layer
Transport Layer
Network Layer
Link Layer
Link Layer : includes device driver and network interface card
Network Layer : handles the movement of packets, i.e. Routing
Transport Layer : provides a reliable flow of data between two hosts
Application Layer : handles the details of the particular application
Notes: <number>

## Slide 8: Packet Encapsulation
The data is sent down the protocol stack
Each layer adds to the data by prepending headers
22Bytes
20Bytes
20Bytes
4Bytes
64 to 1500 Bytes
Notes: <number>

## Slide 9: IP
Responsible for end to end transmission
Sends data in individual packets
Maximum size of packet is determined by the networks
  Fragmented if too large
Unreliable
  Packets might be lost, corrupted, duplicated, delivered out of order

## Slide 10: IP addresses
4 bytes
  e.g. 163.1.125.98
  Each device normally gets one (or more)
  In theory there are about 4 billion available
But…

## Slide 11: Routing
How does a device know where to send a packet?
  All devices need to know what IP addresses are on directly attached networks
  If the destination is on a local network, send it directly there

## Slide 12: Routing (cont)
If the destination address isn’t local
  Most non-router devices just send everything to a single local router
  Routers need to know which network corresponds to each possible IP address

## Slide 13: Allocation of addresses
Controlled centrally by ICANN
  Fairly strict rules on further delegation to avoid wastage
    Have to demonstrate actual need for them
Organizations that got in early have bigger allocations than they really need

## Slide 14: IP packets
Source and destination addresses
Protocol number
  1 = ICMP, 6 = TCP, 17 = UDP
Various options
  e.g. to control fragmentation
Time to live (TTL)
  Prevent routing loops

## Slide 15: IP Datagram
Vers
Len
TOS
Total Length
Identification
Flags
Fragment Offset
TTL
Protocol
Header Checksum
Source Internet Address
Destination Internet Address
Options...
Padding
Data...
0
4
8
16
19
24
31
Field Purpose
Vers IP version number
Len Length of IP header (4 octet units)
TOS Type of Service
T. Length Length of entire datagram (octets)
Ident. IP datagram ID (for frag/reassembly)
Flags Don’t/More fragments
Frag Off Fragment Offset
Field Purpose
TTL Time To Live - Max # of hops
Protocol Higher level protocol (1=ICMP,
6=TCP, 17=UDP)
Checksum Checksum for the IP header
Source IA Originator’s Internet Address
Dest. IA Final Destination Internet Address
Options Source route, time stamp, etc.
Data... Higher level protocol data
You just need to know the IP addresses, TTL and protocol #
Notes: <number>
16

## Slide 16: IP Routing
Routing Table
Destination IP address
IP address of a next-hop router
Flags
Network interface specification
Application
Transport
Network
Link
Application
Transport
Network
Link
Network
Link
Source
Destination
Router
Notes: <number>

## Slide 17: UDP
Thin layer on top of IP
Adds packet length + checksum
  Guard against corrupted packets
Also source and destination ports
  Ports are used to associate a packet with a specific application at each end
Still unreliable:
  Duplication, loss, out-of-orderness possible

## Slide 18: UDP datagram
Destination Port
Source Port
Application data
0
16
31
Checksum
Length
Field Purpose
Source Port 16-bit port number identifying originating application
Destination Port 16-bit port number identifying destination application
Length Length of UDP datagram (UDP header + data)
Checksum Checksum of IP pseudo header, UDP header, and data
Notes: <number>
21

## Slide 19: Typical applications of UDP
  Where packet loss etc is better handled by the application than the network stack
  Where the overhead of setting up a connection isn’t wanted
VOIP
NFS – Network File System
Most games

## Slide 20: TCP
Reliable, full-duplex, connection-oriented, stream delivery
  Interface presented to the application doesn’t require data in individual packets
  Data is guaranteed to arrive, and in the correct order without duplications
    Or the connection will be dropped
  Imposes significant overheads

## Slide 21: Applications of TCP
Most things!
  HTTP, FTP, …
Saves the application a lot of work, so used unless there’s a good reason not to

## Slide 22: TCP implementation
Connections are established using a three-way handshake
Data is divided up into packets by the operating system
Packets are numbered, and received packets are acknowledged
Connections are explicitly closed
  (or may abnormally terminate)

## Slide 23: TCP Packets
Source + destination ports
Sequence number
Acknowledgement number
Checksum
Various options

## Slide 24: TCP Segment
Destination Port
Acknowledgment Number
Options...
Padding
Data...
0
4
10
16
19
24
31
Source Port
Window
Len
Sequence Number
Reserved
Flags
Urgent Pointer
Checksum
Field Purpose
Source Port Identifies originating application
Destination Port Identifies destination application
Sequence Number Sequence number of first octet in the segment
Acknowledgment # Sequence number of the next expected octet (if ACK flag set)
Len Length of TCP header in 4 octet units
Flags TCP flags: SYN, FIN, RST, PSH, ACK, URG
Window Number of octets from ACK that sender will accept
Checksum Checksum of IP pseudo-header + TCP header + data
Urgent Pointer Pointer to end of “urgent data”
Options Special TCP options such as MSS and Window Scale
You just need to know port numbers, seq and ack are added
Notes: <number>
27

## Slide 25: TCP : Data transfer
Host
Client
Send Packet 1
Start Timer
Retransmit Packet1
Start Timer
Packet should arrive
ACK should be sent
ACK would normally
Arrive at this time
Receive Packet 1
Send AXK 1
Time Expires
Receive ACK 1
Cancel Timer
Packet Lost
Timer
Timer

## Slide 26: IPv6
128 bit addresses
  Make it feasible to be very wasteful with address allocations
Lots of other new features
  Built-in autoconfiguration, security options, …
Not really in production use yet

## Slide 27: Ethernet
Computer <-> Computer communication on same network
Each device has unique MAC address (48-bit)
example: 00-C0-4F-48-47-93
Ethernet Packet:
Dest.
address
Data
CRC
Source
address
Type
MAC: Media Access Control
6bytes
6bytes
2bytes
Preamble
8bytes
64 - 1500bytes
4bytes
Do not worry about this slide
Notes: <number>

## Slide 28: ARP : Address Resolution Protocol
ARP provides mapping
  32bit IP address <-> 48bit MAC address
  128.97.89.153 <-> 00-C0-4F-48-47-93
ARP cache
  maintains the recent mappings from IP addresses to MAC addresses
Protocol
ARP request broadcast on Ethernet
Destination host ARP layer responds
Do not worry about this slide
Notes: <number>

## Slide 29: DHCP
Dynamic Host Configuration Protocol
  Used to tell a computer what IP address to use
  Device broadcasts a request from IP 0.0.0.0
    If it had an IP address before, asks for the same one again
  Server (or relay) on local network responds telling it which to use (or ignores it, or tells it go away)
    “Lease time” telling it how long that IP will be valid for
    Device requests renewal of lease after ¾(?) elapsed
Do not worry about this slide