## Slide 1
IP Addressing
Notes: <number>

## Slide 2: IP Addresses
Structure of an IP address
Subnetting
CIDR
IP Version 6 addresses

## Slide 3: IP Addresses

## Slide 4: IP Addresses

## Slide 5: What is an IP Address?
An IP address is a unique global address for a network interface
An IP address:
- is a 32 bit long identifier
- encodes a network number (network prefix)
and a host number

## Slide 6: Dotted Decimal Notation
IP addresses are written in a so-called dotted decimal notation
Each byte is identified by a decimal number in the range [0..255]:
Example:
10001111
10000000
10001001
10010000
1st Byte
= 128
2nd Byte
= 143
3rd Byte
= 137
4th Byte
= 144
128.143.137.144

## Slide 7: Network prefix and Host number
The network prefix identifies a network and the host number identifies a specific host (actually, interface on the network).
How do we know how long the network prefix is?
  The network prefix used to be implicitly defined (class-based addressing, A,B,C,D…)
  The network prefix now is flexible and is indicated by a prefix/netmask (classless).
network prefix
host number

## Slide 8: Example
Example: argon.cs.virginia.edu
IP address is 128.143.137.144
  Is that enough info to route datagram??? -> No, need netmask or prefix at every IP device (host and router)
Using Prefix notation IP address is: 128.143.137.144/16
  Network prefix is 16 bits long
Network mask is: 255.255.0.0 or hex format: ffff0000
  -----> Network id (IP address AND Netmask) is: 128.143.0.0
  -----> Host number (IP address AND inverse of Netmask) is: 137.144
128.143
137.144

## Slide 9: The old way: Classful IP Adresses
When Internet addresses were standardized (early 1980s), the Internet address space was divided up into classes:
  Class A: Network prefix is 8 bits long
  Class B: Network prefix is 16 bits long
  Class C: Network prefix is 24 bits long
Each IP address contained a key which identifies the class:
  Class A: IP address starts with “0”
  Class B: IP address starts with “10”
  Class C: IP address starts with “110”

## Slide 10: The old way: Internet Address Classes

## Slide 11: The old way: Internet Address Classes
We will learn about multicast addresses later in this course.

## Slide 12: Problems with Classful IP Addresses
The original classful address scheme had a number of problems
Problem 1. Too few network addresses for large networks
  Class A and Class B addresses are gone
Problem 2. Two-layer hierarchy is not appropriate for large networks with Class A and Class B addresses.
  Fix #1: Subnetting

## Slide 13: Problems with Classful IP Addresses
Problem 3. Inflexible. Assume a company requires 2,000 addresses
  Class A and B addresses are overkill
  Class C address is insufficient (requires 8 Class C addresses)
  Fix #2: Classless Interdomain Routing (CIDR)

## Slide 14: Problems with Classful IP Addresses
Problem 4: Exploding Routing Tables: Routing on the backbone Internet needs to have an entry for each network address. In 1993, the size of the routing tables started to outgrow the capacity of routers.
  Fix #2: Classless Interdomain Routing (CIDR)

## Slide 15: Problems with Classful IP Addresses
Problem 5. The Internet is going to outgrow the 32-bit addresses
  Fix #3: IP Version 6

## Slide 16: Subnetting
Subnetting
Problem: Organizations have multiple networks which are independently managed
  Solution 1: Allocate an address for each network
    Difficult to manage
    From the outside of the organization, each network must be addressable ie have an identifiable address.
  Solution 2: Add another level of hierarchy to the IP addressing structure
University Network
Medical
School
Library
Engineering
School

## Slide 17: Basic Idea of Subnetting
Split the host number portion of an IP address into a subnet number and a (smaller) host number.
Result is a 3-layer hierarchy
Then:
    Subnets can be freely assigned within the organization
    Internally, subnets are treated as separate networks
    Subnet structure is not visible outside the organization
network prefix
host number
subnet number
network prefix
host number
extended network prefix

## Slide 18: Subnet Masks
Routers and hosts use an extended network prefix (subnet mask) to identify the start of the host numbers
* There are different ways of subnetting. Commonly used netmasks for university networks with /16 prefix (Class B) are 255.255.255.0 and 255.255.0.0

## Slide 19: Example of a Subnetting Plan
Internet
Router
Subnet 1
Subnet 2
R
Subnet 3
Subnet 4
IP Network: 128.49.0.0/16
Subnet 128.49.0.0/24
Subnet 128.49.1.0/25
Subnet 128.49.1.128/25
Subnet 128.49.3.0/24
Subnetwork: 128.49.1.0/24
2 bytes available for subnetting
34=00000000
132=10000000

## Slide 20: Advantages of Subnetting
With subnetting, IP addresses use a 3-layer hierarchy:
        Network
        Subnet
        Host
Improves efficiency of IP addresses by not consuming an entire address space for each physical network.
Reduces router complexity. Since external routers do not know about subnetting, the complexity of routing tables at external routers is reduced.
Note: Length of the subnet mask need not be identical at all subnetworks.
Notes: <number>

## Slide 21: Subnetting Example: Argon

## Slide 22: Network without subnets
128.143.0.0/16

## Slide 23: Same Network with Subnets

## Slide 24: Same network with different subnetmasks
128.143.137.0
Subnet

## Slide 25: Subnetting Example
An organization with 4 departements has the following IP address space: 10.2.22.0/23. As the systems manager, you are required to create subnets to accommodate the IT needs of 4 departments. The subnets have to support to 200, 61, 55, and 41 hosts respectively. What are the 4 subnet network numbers?
Solution:
  10.2.22.0/24 (256 addresses > 200)
  10.2.23.0/26 (64 addresses >61)
  10.2.23.64/26 (64 addresses > 55)
  10.2.23.128/26 (64 addresses > 41)

## Slide 26: CIDR - Classless Interdomain Routing
IP backbone routers have one routing table entry for each network address:
  With subnetting, a backbone router only needs to know one entry for each network
  This is acceptable for Class A and Class B networks
    27 = 128 Class A networks
    214 = 16,384 Class B networks
  But this is not acceptable for Class C networks
    221 = 2,097,152 Class C networks
In 1993, the size of the routing tables started to outgrow the capacity of routers
Consequence: The Class-based assignment of IP addresses had to be abandoned

## Slide 27: CIDR - Classless Interdomain Routing
Goals:
  Restructure IP address assignments to increase efficiency
  Hierarchical routing aggregation to minimize route table entries
Key Concept: The length of the network id (prefix) in IP addresses is arbitrary/flexible and is defined by the network hierarchy.
Consequence:
  Routers use the IP address and the length of the prefix for forwarding.
  All advertised IP addresses must include a prefix

## Slide 28: CIDR Example
CIDR notation of a network address:
192.0.2.0/18
    "18" says that the first 18 bits are the network part of the address
The network part is called the network prefix
Example:
  Assume that a site requires an IP network domain that can support 1000 IP host addresses
  With CIDR, the network is assigned a continuous block of 1024 = 210 (>1000) addresses with a 32-10 = 22-bit long prefix

## Slide 29: CIDR: Prefix Size vs. Host Space
CIDR Block Prefix # of Host Addresses
/27 32 hosts
/26 64 hosts
/25 128 hosts
/24 256 hosts
/23 512 hosts
/22 1,024 hosts
/21 2,048 hosts
/20 4,096 hosts
/19 8,192 hosts
/18 16,384 hosts
/17 32,768 hosts
/16 65,536 hosts
/15 131,072 hosts
/14 262,144 hosts
/13 524,288 hosts

## Slide 30: CIDR and Address assignments
Backbone ISPs obtain large blocks of IP address space and then reallocate portions of their address blocks to their customers.
Example:
Assume that an ISP owns the address block 206.0.64.0/18, which represents 16,384 (232-18=214) IP host addresses
Suppose a client requires 800 host addresses
  512=29<800<1024=210 -> 32-10 = 22,
  Assigning a /22 block, i.e., 206.0.68.0/22 -> gives a block of 1,024 (210) IP addresses to client.

## Slide 31: Subnetting and Classless Inter Domain Routing (CIDR)
Subnetting is done by allocating some of the leading bits of the host number to indicate a subnet number.
  With subnetting, the network prefix and the subnet number make up an extended network prefix.
  The extended prefix can be expressed in terms of a subnetmask or, using CIDR notation, by adding the length of the extended subnetmask after the IP address.
For example, for Argon, the first byte of the host number (the third byte of the IP address) is used to denote the subnet number.
  128.143.0.0/16 is the IP address of the network (network prefix /16),
  128.143.137.0/24 is the IP address of the subnet,
  128.143.137.144/32 is the IP address of the host, and
  255.255.255.0 is the subnetmask of the host (or subnet prefix /24))

## Slide 32: CIDR and Routing Information
206.0.64.0/18
204.188.0.0/15
209.88.232.0/21
Internet Backbone
ISP X owns:
Company X :
206.0.68.0/22
ISP y :
209.88.237.0/24
Organization z1 :
209.88.237.192/26
Organization z2 :
209.88.237.0/26

## Slide 33: CIDR and Routing Information
206.0.64.0/18
204.188.0.0/15
209.88.232.0/21
Internet Backbone
ISP K owns:
Company X :
206.0.68.0/22
ISP Y :
209.88.237.0/24
Organization Z1 :
209.88.237.192/26
Organization Z2 :
209.88.237.0/26
Backbone sends everything which matches the prefixes 206.0.64.0/18, 204.188.0.0/15, 209.88.232.0/21 to ISP K.
ISP K sends everything which matches the prefix: 206.0.68.0/22 to Company X,
209.88.237.0/24 to ISP Y
Backbone routers do not know anything about Company X, ISP Y, or Organizations Z1, Z2.
ISP K does not know about Organizations Z1, Z2.
ISP Y sends everything which matches the prefix: 209.88.237.192/26 to Organizations Z1 209.88.237.0/26 to Organizations Z2

## Slide 34: CIDR and Routing
Aggregation of routing table entries:
  128.143.0.0/16 and 128.142.0.0/16 can be represented as 128.142.0.0/15 at a router.
    143 = 128.10001111.0.0 142 = 128.10001110.0.0
Longest prefix match: Routing table lookup finds the routing entry that matches the longest prefix
  Why????
E.g., What is the outgoing interface for
destination IP address: 128.143.137.0?
Prefix | Interface/outgoing link
128.143.128.0/17 | interface #1
128.128.0.0/9 | interface #2
128.0.0.0/4 | interface #5
Routing table

## Slide 35: IPv6 - IP Version 6
IP Version 6
  Is the successor to the currently used IPv4
  Specification completed in 1994
  Makes improvements to IPv4 (no revolutionary changes)
One (not the only !) feature of IPv6 is a significant increase in size of the IP address to 128 bits (16 bytes)
    IPv6 will solve – for the foreseeable future – the problems with IP addressing

## Slide 36: IPv6 Header

## Slide 37: IPv6 vs. IPv4: Address Comparison
IPv4 has a maximum of
    232  4 billion addresses
IPv6 has a maximum of
  2128 = (232)4  4 billion x 4 billion x 4 billion x 4 billion addresses

## Slide 38: Notation of IPv6 addresses
Convention: The 128-bit IPv6 address is written as eight 16-bit integers (using hexadecimal digits for each integer)
CEDF:BP76:3245:4464:FACE:2E50:3025:DF12
Short notation:
Abbreviations of leading zeroes:
CEDF:BP76:0000:0000:009E:0000:3025:DF12  CEDF:BP76:0:0:9E :0:3025:DF12
“:0000:0000” can be written as “::”
CEDF:BP76:0:0:FACE:0:3025:DF12  CEDF:BP76::FACE:0:3025:DF12
IPv6 addresses derived from IPv4 addresses have different formats. Convention allows to use IPv4 notation for the last 32 bits.
  128.143.137.144 -> 0:0:0:0:0:ffff:808F:8990 or
  128.143.137.144 -> 2002:808f:8990:0:0:0:0:0 (called 6to4 address)

## Slide 39: IPv6 Provider-Based Addresses
The first IPv6 addresses will be allocated to a provider-based plan
Type: Set to “010” for provider-based addresses
Registry: identifies the agency that registered the address
The following fields have a variable length (recommeded length in “()”)
Provider: Id of Internet access provider (16 bits)
Subscriber: Id of the organization at provider (24 bits)
Subnetwork: Id of subnet within organization (32 bits)
Interface: identifies an interface at a node (48 bits)
Registry ID
Provider ID
010
Subscriber ID
Interface ID
Subnetwork ID

## Slide 40: More on IPv6 Addresses
The provider-based addresses have a similar flavor as CIDR addresses
IPv6 provides address formats for:
  Unicast – identifies a single interface
  Multicast – identifies a group. Datagrams sent to a multicast address are sent to all members of the group
  Anycast – identifies a group. Datagrams sent to an anycast address are sent to one of the members in the group.