## Slide 1: Application Layer Functionality and Protocols
Notes: <number>

## Slide 2: Applications Layer – allows user to interface with the network!
Notes: <number>

## Slide 3
Application Layer – Provides the interface between the applications on either end of the network.
Notes: <number>

## Slide 4: Protocols and networks
Notes: <number>

## Slide 5: Protocols
DNS – Matches domain names with IP addresses
HTTP – Used to transfer data between clients/servers using a web browser
SMTP & POP3 – used to send email messages from clients to servers over the internet
FTP – allows the download/upload of files between a client/server
Telnet – allows users to login to a host from a remote location and take control as if they were sitting at the machine (virtual connection)
DHCP – assigns IP addresses, subnet masks, default gateways, DNS servers, etcs. To users as they login the network
Notes: <number>

## Slide 6: Application layer software
2 types
  Applications – Provide the human (user) interface. Relies on lower layers to complete the communication process.
  Services – establish an interface to the network where protocols provide the rules and formats that govern how data is treated..
Notes: <number>

## Slide 7: How data requests occur & are filled
Client/server model
  Advantages:
  Centralized administration
  Security is easier to enforce
Application layer services and protocols
Peer-to-peer networking and applications
Notes: <number>

## Slide 8: Client/Server Model
Client –
  device requesting information (initiates the data exchange)
  Can also UPLOAD data to the servers
Server – device responding to the request
  How does it handle multiple request from multiple users and keep everything in order?
  Relies on support from the lower layer functions to distinguish between services and conversations.
  Server relies on a service called a server daemon – runs in the background and ‘listens’ for requests for that service. It can then exchange messages as appropriate & send requested data.
Examples:
  E-mail Client on an employee computer issues a request to the e-mail server for any unread e-mail. The server responds by sending the e-mail to the client.
  Conversations can originate with either party.
Notes: <number>

## Slide 9: Peer-to-Peer (P2P) Network Model
Two or more computers are connected and are able to share resources without having a dedicated server
Every end device can function as a client or server on a ‘per request’ basis
Resources are decentralized (information can be located anywhere)
Difficult to enforce security and policies
User accounts and access rights have to be set individually on each peer device
Notes: <number>

## Slide 10: P2P Applications
Running applications in hybrid mode allows for a centralized directory of files even though the files themselves may be on multiple machines
Unlike P2P networks, a device can act as both the client and server within the same communication
Each device must provide a user interface and run a background service.
Can be used on P2P networks, client/server networks and across the internet.
Notes: <number>

## Slide 11: P2P Applications Example
Notes: <number>

## Slide 12: Common Port Numbers
TCP
  FTP – 20-21
  Telnet – 23
  SMTP – 25
  DNS – 53 (Both TCP & UDP)
  HTTP – 80
UDP
  DHCP – 67 & 68
  POP – 110
Notes: <number>

## Slide 13: DNS Services
DNS resolver – supports name resolution for other network applications and services that need it.
Devices are usually given 1 or more DNS Server addresses they can use for name resolution.
Uses different types of resource records to actually resolve the name/IP address issues
Notes: <number>

## Slide 14: DSN Services and Protocol
DNS Servers resolve names to IP addresses. It would be difficult to remember the IP address of every website we like to visit, but we can remember names.
THANK YOU DNS SERVER!
Notes: <number>

## Slide 15: WWW Service and HTTP
Steps:
  1) URL is typed in the address bar.
  Browser checks with DNS server to convert it to an IP address
  Connects to the server requested
  Using HTTP or HTTPS protocol requirements, the browser sends a GET request to the server to ask for the desired html document (usually index.html)
  The server sends the HTML code for the web page to the browser.
  The browser interprets the HTML code and formats the page to fit the browser window.
  See the next slide for an example.
Notes: <number>

## Slide 16: WWW Service and HTTP
HTTP/HTTPS are some of the MOST used application protocols!
Notes: <number>

## Slide 17: E-mail services and SMTP/POP protocols
E-mail is the most popular network service.
E-mail client (when people compose e-mail) is called Mail User Agent (MUA)
MUA allows messages to be sent/retrieved to and from your mailbox
Requires several applications and services
  POP or POP3 – deliver email from server to client (incoming messages)
  SMTP – handles outbound messages from clients
Notes: <number>

## Slide 18: E-mail services and SMTP/POP protocols
What do servers require?
  Must be running SMTP!
  Also operates
    Mail Transfer Agent (MTA) – used to forward email
      Receives email from the clients MUA
      Uses SMTP to route email between SERVERS!
      Passes email to the MDA for final delivery
    Mail Delivery Agent (MDA) – receives messages from MUA or from the MTA on another server
  For two e-mail servers to talk – MUST run SMTP and MTA in order to transfer mail between the 2 servers!
  Some clients run Lotus Notes, Groupwise, or MS Exchange. They have their own proprietary protocol for handling e-mail.
Notes: <number>

## Slide 19: E-mail services and SMTP/POP protocols
Notes: <number>

## Slide 20: FTP
Commonly used application layer protocol
Allows for the transfer of files between clients/servers.
Requires 2 connections to the server
  Commands – uses TCP port 21
  Actual data – uses TCP port 20
Notes: <number>

## Slide 21: DHCP
Dynamic Host Configuration Protocol – enables devices to obtain IP addresses, subnet masks, gateways, DNS server information, etc. from a DHCP server.
An IP address that is not being used is assigned from a range of available addresses
Not permanently assigned – only leased for a specific period of time (usually 24 hours – 7 days)
If the host logs off or the power is lost, the IP address they were using is returned to the pool to be re-assigned to another host when needed.
This is how you are able to use Wi-Fi at various places in the world!
Don’t use DHCP for devices such as servers, printers, routers, switches, etc. These should be statically assigned.
This will be covered in greater detail in CCNA 4.
Notes: <number>

## Slide 22: Telnet
Developed in the early 1970’s – among the oldest of the application layer protocols and services in the TCP/IP protocol suite.
Allows users to emulate text-based terminal devices over the network using software.
A connection is known as a ‘virtual terminal (vty)’ session.
Can be run from the command prompt on a PC.
You can use the device as if you were sitting there with all the rights and priorities that you username will offer you.
Disadvantages: Doesn’t support encryption like SSH. All data is transferred as plain text. It can be easily intercepted and understood.
If security is a concern, you should use Secure Shell (SSH) protocol. Provides for remote logins with stronger authentication than telnet.
Network Professionals should always use SSH whenever possible.
Notes: <number>

## Slide 23: Telnet
Notes: <number>

## Slide 24: File Sharing Services and SMB protocol
Server Message Block
SMB has become a mainstay of Microsoft networking, even more so since the introduction of Windows 2000 software.
Allows servers to share their resources with clients
Linux and Unix also share with Microsoft networks using a version of SMB called SAMBA.
Apple also supports sharing resources using an SMB protocol
What can SMB do?
  Start, authenticate, and terminate sessions
  Control file and printer access
  Allow applications to send/receive messages to/from another device
Notes: <number>

## Slide 25: File sharing services and SMB
Notes: <number>