## Slide 1: Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 11
Predetermined Motion Time System (PMTS)
1

## Slide 2: Introduction
Definition: PMTS are systems used to establish labor standards by breaking down tasks into basic motions (reach, grasp, move, release).
Purpose: Allows for accurate measurement and standardization without direct time studies.
Procedure:
Synthesize the method using basic motion elements.
Obtain and sum normal time values from PMTS tables.
Evaluate and improve the method.
Apply allowances to determine the standard time.
Key Systems: MTM and MOST.
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Methods-Time Measurement (MTM)
Overview: MTM is a widely used PMTS, developed in 1948, with various systems (MTM-1, MTM-2, etc.) suited for different tasks.
MTM Systems:
MTM-1: Detailed, for highly repetitive tasks
MTM-2: Simplified, for less repetitive tasks
MTM-3: Broad categories, for longer cycle tasks
MTM-V: For variable environments
MTM-SAM: For standard repetitive tasks
Examples: MTM-1 for assembly line tasks, MTM-2 for worker performing machine operations, MTM-3 for administrative tasks.
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: First-Level PMTS vs. Higher-Level PMTS
First-Level PMTS:
Uses basic motion elements like reach, grasp, release.
Highly detailed with body motions.
Higher-Level PMTS:
Combines basic motions into sequences.
Condensed databases with fewer specified motions, longer normal times.
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Motion Aggregates
Definition: A combination of several basic motions into a sequence.
Example: "Lay an object down" includes reach and release motions.
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Time Units in Methods-Time Measurement
TMU (Time Measurement Unit):
1 TMU = 0.00001 hr = 0.036 sec.
Used to calculate normal time in MTM.
Conversion: 1 sec = 27.8 TMU
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Advantages of Higher-Level PMTS
Faster Application: Higher-level PMTS are quicker to apply than first-level PMTS.
Example: An application speed ratio of 50 means it takes 50 minutes to determine a 1-minute time standard.
Longer Cycle Times: Suitable for tasks with longer cycle times.
Ease of Use: Easier to apply in various settings.
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: MTM Procedure
Steps:
Analyze the task into basic motions (e.g., reach, grasp).
Assign TMU time standards from MTM tables.
Sum TMUs and convert to seconds.
No Performance Ratings: MTM table values are normalized, eliminating the need for performance ratings.
Example Calculations:
Reach, Move, Walking sequences with TMU and time conversion.
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Maynard Operation Sequence Technique (MOST)
Overview: Developed by Zjell Zandin, MOST is faster and more efficient than MTM.
Types:
BasicMOST: For general tasks
MiniMOST: For short-cycle, repetitive tasks
MaxiMOST: For long-cycle, non-repetitive tasks
Application: Breaks down tasks into activity sequences rather than individual motions, reducing the time required for standardization.
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Basic MOST
Focus: Work involving movement of objects (e.g., parts, tools).
MOST Procedure:
Analyze tasks into activity sequence models
Assign time standards from sequence model tables
Sum index values and multiply by 10 to get TMUs
Example: Office worker picking up a file, walking, and placing it on a desk.
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: MOST Software
Overview: Software tools expedite the computation of activity sequence models.
Example: Input values in MOST software, demonstrating ease of use and quick calculations.
Chapter 11 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11