## Slide 1: Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 12
Standard Data Systems
1

## Slide 2: Introduction
Definition: A standard data system is a structured method for collecting, analyzing, and using data related to work processes to create a database of normal time values.
Purpose: Ensures consistency, accuracy, and reliability in measuring and improving productivity and efficiency.
Components: Includes predefined times and methods for tasks, using direct time study and PMTS as benchmarks.
Applications: Useful for tasks with similarities, batch production, large volume standards, and setting standards before production begins.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: How to Create a Standard Data System
Identify Scope and Objectives: Define processes and objectives (e.g., improving productivity, reducing cycle time).
Conduct Work Studies: Perform time and motion studies, break tasks into elemental motions, and measure time for each.
Establish Standard Time: Calculate standard times, adjust for allowances like breaks and delays.
Develop SOPs: Document best practices and methods, create detailed SOPs.
Implement Data Collection Systems: Set up systems for consistent and accurate data collection.
Analyze and Update Data: Regularly review data, identify trends, update standard times, and SOPs.
Train Employees: Train workers on new standards and procedures.
Monitor and Enforce Standards: Continuously monitor performance, provide feedback, and ensure compliance.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: How to Use a Standard Data System
Steps:
Analyze the task and divide it into distinct work elements.
Refer to the database for normal time values of work elements.
Sum the work element normal times to obtain the total normal time.
Add an appropriate allowance factor to get the standard time.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Different Classifications of Work Elements in Standard Data Systems (Part 1)
Setup and Production Work Elements:
Setup elements occur once per batch, while production work elements occur per work unit.
Equation (Total batch time):
Constant and Variable Work Elements:
Constant elements maintain the same time value; variable elements' time varies due to work variables.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Different Classifications of Work Elements in Standard Data Systems (Part 2)
Operator-Paced and Machine-Controlled Work Elements:
Operator-paced involve manual activities, machine-paced depend on machine parameters.
      Regular and Irregular Work Elements:
Regular occur every cycle, irregular occur less frequently.
Internal and External Work Elements:
Internal performed when the machine is stopped, external performed while the machine runs.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Standard Data for Work Cycles
When to Study Entire Task:
When individual work element times are highly variable.
Elements overlap or are difficult to separate.
Several elements involved in the task, used to compare worker performance.
Examples:
Income tax report preparation, supermarket checkout, document proofreading.
Advantages:
Time and labor savings, simpler predictive model, accuracy similar to detailed approaches.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Examples of a Standard Data System (Part 1)
Example 1: Corrugated Boxes Manufacturing:
Objectives: Reduce production time, ensure consistent quality.
Work Studies: Analyze tasks like cutting, folding, gluing.
Standard Time: Calculate and update as processes change.
SOPs: Document best practices, implement time-tracking systems.
Training & Monitoring: Regularly train employees, monitor compliance.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Examples of a Standard Data System (Part 2)
Example 2: Smartphone Assembly Line:
Objectives: Reduce cycle time, increase output.
Work Studies: Analyze tasks like component placement, soldering.
Data Collection: Use real-time tracking tools, analyze and update regularly.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Examples of a Standard Data System (Part 3)
Example 3: Preparing Monthly Profit and Loss Statement:
Objectives: Reduce preparation time, ensure accuracy.
Work Studies: Analyze tasks like data collection, entry, reconciliation.
SOPs: Document best practices, ensure compliance through monitoring.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Advantages of Standard Data Systems
Improved Productivity: Clear benchmarks and best practices.
Consistency: Uniform task performance reduces variability.
Efficiency: Reduces time, optimizes workflows.
Cost Control: Accurate labor cost estimation.
Training & Process Improvement: Simplified training, continuous improvement.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11

## Slide 12: Disadvantages of Standard Data Systems
High Investment Cost: Time and cost resources needed.
Rigidity: Lack of flexibility in operations.
Maintenance: Regular updates required.
Inaccurate Data Risk: Flawed initial data leads to inefficiencies.
Complexity: Challenging for large, diverse operations.
Chapter 12 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
12