## Slide 1: Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 8
Performance Rating
1

## Slide 2: Introduction
What is Performance Rating?
Analysts evaluate employee performance during a time study.
Performance is compared to the analyst's perception of "normal" working speed.
Why Use Performance Rating?
Employees work at varying speeds (average, slow, fast).
Adjusts time standards to reflect the average trained worker's speed.
A skilled analyst can determine standard time regardless of worker speed.
Performance rating is subjective, relying on the analyst’s judgment and experience. The observed time is adjusted by the performance rating to calculate normal time. Job difficulty and conditions influence the analyst's perception of normal pace.
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Accuracy of Performance Rating
Performance rating is a controversial topic in time study standards.
All standards have some error, but they must be accurate enough for practical application.
Accuracy Levels by Application:
Applications:
Incentive Pay Rates: Used for paying employees per unit produced. Accuracy is critical to ensure fair pay distribution.
Day Work Standards: Establish daily quotas. Minor deviations are acceptable as long as the weekly average balances.
Costing and Planning Standards: Used for bookkeeping, not directly affecting employee pay or daily output.
Application | Accuracy
Incentive Pay Piece Rates | +/- 5%
Day Work Quota Standards | +/- 10%
Costing and Planning | +/- 15%
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Rating Methods
Entire Job Rating: Single rating for the whole job
Element-by-Element Rating: Each element gets its own rating
Individual Time Rating: Each recorded time value is rated separately
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Normal Performance Concepts
Defining 100% Productivity:
High Task Standard:
  100% at the mean of the bell curve.
                50% of employees fall below this standard.
                Example: 20 sec/cycle = $132/day.
Low Task Standard:
                100% near the right end of the bell curve.
                95% of employees meet or exceed this standard.
                Example: 24 sec/cycle = $110/day.
Labor Cost: Both standards result in the same payroll cost per part produced.
Employee Morale:
High Task Standard: Only 50% meet the standard, potentially harming morale.
Low Task Standard: 95% meet the standard, boosting morale and self-image.
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: The Point Factor Rating Method
Defines job characteristics/elements
Assigns degrees and point values
Total job value = sum of assigned points
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: The Westinghouse System
Four Factors:
Skill: Proficiency in following the given method
Effort: Will to work
Environment: General work surroundings
Consistency: Performance consistency
Final Rating = Sum of four factors + 100%
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Benchmark Standards
Walking:
3 mph: 50 feet in 11.3 seconds (27-inch stride)
3.57 mph: Unobstructed area, 34-inch stride (MTM Guideline)
Dealing:
52 cards into 4 piles: 30 seconds (left hand holds, right hand delivers)
Performance Rating:
100% Productivity: Average trained employee’s speed
Below 100%: Slower than average
Above 100%: Faster than average
Rate Speed: Compare to average
Focus on speed of walking or hand movements
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Walking Rating Practice
Benchmark:
3 mph: 50 feet in 11.3 seconds (27-inch stride)
Setup:
Measure 60 feet: 50 feet for timing, 5 feet for start/stop
Start walking, time the middle 50 feet with a stopwatch
Steps:
Start walking, begin timing at the start of the 50-foot mark.
Stop timing at the end of the 50-foot mark.
Estimate walking speed as a percentage of 100% and record
Record actual time in "Stopwatch Time"
Leveled Rating = (11.3 seconds / Stopwatch Time) x 100
Difference = My Rating - Leveled Rating
Objective: Aim for zero difference between estimated and leveled ratings.
Ratings should be in multiples of fives.
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Hand Motion Rating Practice
Benchmark:
Dealing 52 cards into 4 piles in 30 seconds (0.500 minutes)
Setup:
Left hand holds and pushes cards forward.
Right hand delivers cards to four stacks.
Steps:
Start: Have a friend time you
Deal: Begin dealing when "Start" is called
Stop: Friend stops stopwatch when last card is placed
Estimate Speed: Write down estimated speed
Leveled Rating = (30 seconds / Stopwatch Time) x 100
Difference = My Rating - Leveled Rating
Objective: Aim for zero difference between estimated and leveled ratings.
Positive difference: Overestimation. Negative difference: Underestimation.
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Calculating the Performance Rating – Part 1
Example 1: Performance Rating Calculation
    Observed Times (min):
    Element a: 0.32
    Element b: 0.20
    Element c: 0.62 (machine-controlled)
    Element d: 0.47
    Normal Time:
    Normal Time for Cycle:
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11

## Slide 12: Calculating the Performance Rating – Part 2
    Standard Time:
    Worker Performance:
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
12

## Slide 13: Calculating the Performance Rating – Part 3
    Example 2: Performance Rating of Walking
    Benchmark: 3.0 mi/hr
    Performance: Walking 2.5 miles in 45 minutes
Chapter 8 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
13