## Slide 1: Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
1
Chapter 3
Manual Work

## Slide 2: Introduction to Work Systems
A work unit is any object processed by a work system, such as a machined workpiece, moved material, customer in a store, or designed product.
Three categories:
Manual work system: when one or more tasks are performed by human workers without machinery or automation.
Worker-machine system: performed by a worker who operates power tools.
Automated work system: performed by a worker who operates power tools.
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Manual Work Systems
Manual work system is when one or more tasks are performed by human workers without machinery or automation. Tasks are simple repetitive actions to complex operations. Manual work can be performed with or without hand tools. When using hand tools, the power comes from the worker's strength and stamina.
Examples of pure manual work:
Material handler moving cartons
Assembly worker putting together parts
Creating products by hand (pottery, woodworking)
Office worker filing documents
Manually inspecting products
Manually packing products
Examples of manual work with hand tools:
Machinist filing a part
Assembly worker using a screwdriver
Painter using a paintbrush
QC inspector using a micrometer
Material handling worker using a dolly
Office worker writing with a pen
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Worker Performance
Worker performance is the pace or speed of working. Higher performance decreases cycle time, which is desirable for employers.
Performance rating is the worker's pace observed by a trained time study analyst, recorded as a percentage, and used as a decimal in the normal time, Tn, equation.
Performance Rating (PR):
Faster pace: PR > 100%
Standard pace: PR = 100%
Slower pace: PR < 100%
Example calculation:
Normal time = Tn = 6.5 sec
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Normal Performance and Normal Time
Normal performance is pace maintained by an average worker without adverse health effects.
Normal time is the time needed to complete a task under standard conditions, without delays. It depends on the worker's pace.
Example calculations:
Normal Time: If the observed time for a task is 8.25 minutes and the performance rating is 1.1 (110%), what is the normal time?
Cycle Time for Repetitive Work: If a worker assembles a product in 5 minutes and performs quality checks in 2 minutes, both at a normal pace, the cycle time is:
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Standard Performance and Standard Time
Standard performance: Normal performance with periodic rest breaks.
PFD Allowance: Accounts for personal time (P), fatigue (F), and delays (D).
Standard time: Normal time + allowances for personal time, fatigue, and delays.
Example calculation:
If the normal time is 8.8 minutes and the allowance factor is 15%, what is the standard time per unit?
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Irregular Work Elements (Part 1)
Irregular work elements are infrequent tasks during a process. They are prorated into the regular cycle.
Examples:
Changing a tool
Swapping pallets or tote pans
Changing a machine setup
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Irregular Work Elements (Part 2)
Example calculations:
The normal time to perform a certain manual work cycle is 4.25 min. In addition, an irregular work element whose normal time is 3.5 min must be performed every 20 cycles. One work unit is produced each cycle. The PFD allowance factor is 12%. The worker’s pace is 105%.
Determine the standard time per unit:
What is the cycle time?
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Foreign Work Elements
Foreign work elements are unplanned tasks outside of the standard process.
Examples:
Responding to unexpected machine breakdown
Responding to urgent or unexpected requests
Responding to process anomalies
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Worker-Machine Systems (Part 1)
Worker-machine systems are tasks shared between human workers and machines.
Examples:
Construction worker operating a front-end loader
Truck driver driving an 18-wheeler
Forklift driver operating a forklift
Clerical worker entering data into a PC
Types of powered equipment:
Portable power tools
Mobile powered equipment
Stationary powered equipment
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Worker-Machine Systems (Part 2)
Number of workers and machines:
One worker-one machine
One worker-multiple machines
Multiple workers-one machine
Multiple workers-multiple machines
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11

## Slide 12: Worker-Machine Systems (Part 3)
Level of Operator Attention:
Full-time attention
Part-time attention during each work cycle
Part-time attention with regular servicing
Periodic attention with random servicing
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
12

## Slide 13: Cycle Time Analysis
Cycle time analysis involves two types of worker-machine systems:
Machine time depends on operator control
Machine time is constant and independent
Formulas:
Cycle time with no overlap:
Standard time for cycle:
Example calculation:
A wage incentive plan pays workers a daily wage at a rate of $20.00/hr multiplied by the number of hours worked during the shift. One worker-machine task in the plant includes worker-paced elements totaling a normal time of 1.25 minutes and machine-paced elements with a time of 2.00 minutes. The PFD allowance is 15%. Determine the standard time for the task given that Am = 25%.
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
13

## Slide 14: Cycle Time vs. Production Rate
Inverse relationship between cycle time (Tc) and production rate (Rp)
Example calculations:
If Tc = 6 sec/unit, then what is the production rate?
If Rp = 600 pc/hr, then what is the cycle time?
Chapter 3 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
14