## Slide 1: Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 2
Charting and Diagramming Techniques
1

## Slide 2: Introduction to Charting and Diagramming Techniques
Charting and diagramming techniques visually summarize activities to analyze work processes, helping engineers design and improve production and delivery by identifying and eliminating waste, thus enhancing efficiency and productivity.
Purpose:
Graphically illustrate and summarize work processes
Useful for methods engineering and operations analysis
Objectives:
Communicate work processes effectively
Use algorithms for specific diagramming techniques
Divide work processes into distinct elements for analysis
Provide a structure for improvements
Represent existing or proposed work processes
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Creating Charts and Diagrams
Any combination of the following techniques can be used to develop a description of the work process that is used to create a chart or diagram:
Techniques:
Analyst familiar with the process, creates a graphic and asks others to review the graphic
Analyst observes the process, develops a chart/diagram and asks others to review the graphic
Analyst conducts one-on-one interviews with people familiar with the process to create a chart/diagram and asks others to review the graphic
Analysts arranges a group meeting facilitated by a skilled moderator to gather input and create a chart/diagram based on notes from the group discussion and asks others to review the graphic
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Traditional Industrial Engineering Charting Techniques
Common charting and diagramming techniques used to analyze an existing operation, sequence of operations, or present proposals for new ways of accomplishing the same operations, or design new operations that have not been performed previously.
Five Basic Symbols:
Operation (O): Circle; altering physical/chemical characteristics, assembly, planning
Inspection (I): Diamond; examining objects for quality or quantity.
Transportation (T): Arrow; moving objects/data
Delay (D): Capital D; temporarily setting aside an object
Storage (S): Triangle; intentionally setting aside an object for protection
Combined Activity: When performing two or more activities simultaneously, the symbols for those activities are combined. An example is when an employee operates on an object and then inspects it for quality, it is symbolized as "OI“.
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Network Diagrams
A network diagram includes:
Nodes: Represent operations, work elements or entities/tasks
Arrows: Connect nodes to show relationships, indicate workflow direction or precedence order
Example Calculations:
For two-way flows between nodes:
For one-way arrows:
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Operation Process Chart (Part 1)
An Operation Process Chart is a graphic representation highlighting the operations and inspections involved in producing a product or providing a service.
Rules to construct chart:
At top of page:
      Include analyst’s name, date, operation name and all additional information such as total number of operations and inspections
      Draw a simple product sketch
Only use symbols O & I (circle for operations, diamond for inspections)
If a combined activity, draw a circle inside the diamond
If numbered, place numbers inside the circle or diamond
Sequence activities from top to bottom in order of occurrence
Show merging assembly lines side-by-side
Connect symbols with straight lines to indicate activity sequence
Write material above a horizontal line entering from the left; connect to the operation symbol
List each material on separate horizontal lines attached to the entry point.
Write a brief description on the right side of each symbol.
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Operation Process Chart (Part 2)
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Flow Process Chart (Part 1)
A Flow Process Chart graphically represents all activities involved in manufacturing a product or providing a service, highlighting non-value-added activities for evaluation.
Rules to construct chart:
Create separate chart for each major phase of a complicated process
Add pages if necessary
At top of page: include analyst's name, date, operation name, operator's name, and equipment description in header; add extra information if needed
List work in sequential order from top to bottom
Number steps sequentially
Use symbols for operations, inspections, transportations, delays, and storages
Indicate quantities if appropriate
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Flow Process Chart (Part 2)
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Flow Diagram
After creating a Flow Process Chart, illustrate the process on a scale drawing of the work area as a Flow Diagram. Include the title "Flow Diagram," analyst's name, date, operation name, and scale. Use the same numbering sequence and symbols from the Flow Process Chart.
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Left Hand - Right Hand (LH-RH) Chart (Part 1)
A Left Hand – Right Hand Chart maximizes efficiency and implements ergonomic principles of motion economy. This chart shows the simultaneous use of both hands during a task to precisely identify current performance methods.
Rules to construct chart:
Observe the operation and document steps using standard charting symbols (operations, inspections, transportations, delays, and storages)
    List steps sequentially
    Record transportation distances for each hand
    Indicate simultaneous motions
    Show idle time for each hand
Draw a detailed, to-scale sketch of work area on the back of the chart, showing the work surface, bins, containers, materials, tools, equipment, and the employee
Analyze and improve the current method by reducing idle time, using fixtures to free hands, minimizing reach distances, increasing simultaneous motions, and eliminating ineffective motions like searching, positioning, and thinking time.
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11

## Slide 12: Left Hand - Right Hand (LH-RH) Chart (Part 2)
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
12

## Slide 13: Multiple Activity Chart (Part 1)
A Multiple Activity Chart shows the breakdown of a process over time, showing interdependent work relationships.
Benefits:
Identify and reduce idle time
Balance work distribution
Eliminate unnecessary activities
Establish optimal number of machines per person/team
Permits a detailed analysis of the potential impact
Provides a clear visual comparison between current and proposed methods
Rules to construct chart:
Document the current method as baseline
Use multiple columns as needed, labeling each for a person or machine
Label the time scale with a single unit and appropriate increments
Record work and idle times sequentially for each column
Analyze and improve the method by minimizing idle time, optimizing the use of costly or scarce components, and reducing operating costs or cycle time
Compare alternatives and select the best option
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
13

## Slide 14: Multiple Activity Chart (Part 2)
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
14

## Slide 15: Basic Process Map
A Basic Process Map (aka Flow Chart) visually shows the inputs, activities, and outputs of a process, showing the raw materials/resources, steps taken, and the completed product or service.
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
15

## Slide 16: From-To Chart
A From-To chart shows relationships between points, such as mileage between cities or material flow between plant areas.
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
16

## Slide 17: Activity Relationship Chart
An Activity Relationship Chart arranges the closeness ratings among activities or departments using six ratings.
Ratings:
A: Absolutely necessary
E: Especially important
I: Important
O: Ordinary closeness
U: Unnecessary
X: Avoid closeness
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
17

## Slide 18: Relationship Process Map
A Relationship Process Map is a block diagram that illustrates the input-output connections among an organization's departments or functional components.
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
18

## Slide 19: SIPOC Diagram
A SIPOC diagram visually documents a process from start to finish, aiming to identify results, inefficiencies, and provoke improvements by providing a high-level overview and encouraging the definition of new processes.
Example
Chapter 2 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
19