## Slide 1: Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 7
Allowance for Personal Time, Fatigue, and Delays (PFD)
1

## Slide 2: Introduction
Most time studies are collected on hourly-paid employees. Time study results determine pay, job difficulty, and job variety.
Two basic pay methods:
Time-based (rate per hour)
Unit-based (rate per piece of completed work)
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Daywork
Employees are paid an hourly rate regardless of output. No quotas are established; production may vary daily.
Pay rates vary based on:
Skill
Learning time
Decision impact
And other factors
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Measured Daywork
Employees receive a flat rate for a day's work.
Standard output is established for planning and efficiency measurement.
Employees are paid the flat rate regardless of actual output.
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Standard Hour Plan
Employees have a minimum base rate of pay linked to a target output.
For each 1% increase in output over the target, a 1% premium is paid.
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Piecework
Oldest payment method: pay is tied to the number of units produced.
Time-studied standards determine pay, ensuring it relates to work done.
Employees are guaranteed a minimum wage in the USA, even with low output.
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Allowance for Personal Fatigue and Delay (PFD)
PFD allowances ensure time standards are realistic and achievable.
Helps prevent worker overburdening, maintaining sustainable work pace.
Personal Time (P):
Accounts for personal needs (e.g., restroom breaks, hydration)
Typical allowance: 5% of total time
Fatigue (F):
Compensates for physical and mental fatigue due to work
Typical allowance: 4-8%, depending on work demands
Delay (D):
Covers unavoidable delays like machine breakdowns, material shortages
Typical allowance: 2-5%, based on delay frequency and nature
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Calculating the PFD Allowance
Formula: [ 1 / (1 - PFD Ratio) ] – 1
Example:
Total PFD Time Ratio = 0.131
PFD Allowance = [1 / (1 - 0.131)] – 1 = 15.1%
Therefore, when the total normal time per unit is multiplied by 15%, this allows for 13.1% (or 0.131 x 480 min = 62.88 min) of the 8-hour workday for P, F, and D issues.
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Apfd Alternative Formula
Formula:
Example:
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Rest Allowances
Rest allowances are critical but difficult to standardize globally. ILO recommendations include personal allowance, basic fatigue allowance, and variable allowances.
Challenges in Establishing Universal Allowance Guidelines (ILO):
Individual Factors: Work ethic, learning curves, ethnic differences, and worker nourishment.
Work Nature: Work type (light, medium, heavy), standing vs. sitting, posture, required force, mental/eye strain, use of protective gear, and risk of product damage.
Environmental Factors: Heat, humidity, noise, dirt, vibration, lighting, dust, wet and seasonal conditions.
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Determining & Applying Percentages
Percentages can be determined using these techniques:
1. Historical time studies
2. Work sampling
3. Experience estimates
4. Management directives
Percentages can be applied to:
1. Entire plant (common practice)
2. Specific departments
3. Individual jobs
Typical percentages in industry range from 7.5% - 20%.
Manufacturing often uses 15%
Service sectors range from 25% - 100% (common is 50%)
Final percentages are usually rounded to the nearest 2.5%.
Chapter 7 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11