## Slide 1: Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 5
Manual Assembly Lines
1

## Slide 2: Introduction to Manual Assembly Lines
Manual assembly lines are production lines where products are assembled along the assembly line by workers performing specific tasks sequentially.
Use of manual or powered conveyors.
High productivity achieved through:
job specialization
reduced handling
flow of work
standardization
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Key Features of Manual Assembly Lines
Products move along the line with work completed at each workstation.
Base parts are launched at regular intervals.
Successive workstations progressively add components.
Manual Lines:
Products are manually passed between stations
Mechanized Conveyors:
Belt-driven or chain-driven systems move parts along the line
Mechanized Transport Systems:
Floor, waist-high, and overhead conveyors
Automated Guided Vehicles (AGVs)
Other transport mechanisms
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Workstations and Manning Level
Workstation is a specific location where tasks are performed by a worker.
Manning level is the number of workers assigned per workstation.
Scenario: If a production line consists of 20 workstations and has 24 workers, what is the manning level?
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Work Transport Systems
Manual and mechanized movement move materials along the assembly line.
Potential Issues:
  Starving: Task completed, but next unit hasn't arrived.
  Blocking: Task completed, but can't pass unit to next station.
Mechanized Handling Equipment: Includes powered conveyors and other types of equipment.
Parts Movement:
Synchronous (Paced): Moves at fixed intervals.
Asynchronous (Unpaced): Moves independently.
Work Transport Systems:
Continuous Transport
Synchronous Transport
Asynchronous Transport
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Continuous Transport System
Continuous transport system is steady, unbroken movement of materials/products along a predefined path.
Characteristics:
continuous material flow
ideal for high-volume repetitive processes
reduced handling and waiting time
minimizes idle time and ensures consistent workflow
commonly used in assembly lines, mining, and bulk transport
Examples: Conveyor belts, pipelines, AGVs.
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Synchronized Transport System
Synchronized transport system moves materials/products at predetermined, paced intervals for system harmony.
Characteristics:
Fixed interval movement synchronized with production cycles.
Coordination ensures timely material flow.
Reduces bottlenecks and balances workload across stations.
Examples: Automotive manufacturing & other high-volume production environments.
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Asynchronous Transport System
Asynchronous transport system is where materials/products move independently (unpaced) through production without a fixed schedule.
Characteristics:
Flexible movement based on process requirements.
Allows variability in production times and processes.
Reduces delays from synchronization issues.
Ideal for low-volume, customized, or batch production with varying task times.
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Comparison of Work Transport Systems
Continuous: Best for high-volume uninterrupted processes.
Synchronized: Ideal for high-volume fixed-cycle production.
Asynchronous: Most suitable for variable low-volume or customized production.
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Working with Product Variety
Types of manual assembly lines:
Single Model
Produces one type of product
Identical tasks at each workstation
Example: Car assembly line
Batch Model
Produces different products in batches
Economical for multiple products on one line
Example: Phone models in batches
Mixed Model:
Produces different models simultaneously
No need for setup changes between models
Examples: Automobiles, appliances, laptops
Mixed Model vs. Batch Model:
Advantages: No downtime between model changes; adaptable to demand changes.
Disadvantages: More complex task assignment for balanced workloads.
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Common Metrics for Assembly Lines
Annual Demand ()
Hourly Production Rate ()
Cycle Time ()
Formulas:
Example Calculation: If cycle time equals 4.0 sec/pc, what is the production rate?
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11

## Slide 12: Work Content Time
Work content time () is the total time required to assemble one unit.
Formula:
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
12

## Slide 13: Number of Workers Required
Expressed in two different ways:
Theoretical
Actual
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
13

## Slide 14: Repositioning Losses
Repositioning time is the time lost due to repositioning a worker, unit or both. Example: In a U-shaped work cell, after starting a machine cycle, a worker must reposition to operate another machine.
Service time is the cycle time minus repositioning time.
Repositioning efficiency represents the loss of productive assembly time due to repositioning.
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
14

## Slide 15: Line Balance Efficiency
Perfect line balance is nearly impossible due to varying work element times and constraints. Line balance efficiency, calculated as work content time / total available service time = measures balance quality.
Balance delay, the complement of line balance efficiency, indicates time lost due to imperfect balancing as a ratio of total available time.
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
15

## Slide 16: Worker Requirements
Factors Affecting Assembly Line Productivity:
Line Efficiency (E)
Repositioning Efficiency (Er)
Line Balance Efficiency (Eb)
Combined, these factors determine overall labor efficiency
Using this measure, we can calculate the actual number of workers needed on the assembly line:
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
16

## Slide 17: Workstation Considerations
A workstation is a position on the assembly line where tasks are performed.
If each workstation has one worker, the number of workstations equals the number of workers:
Cycle time is determined by spacing and conveyor speed:
Total line length is calculated by number of workstations and length of each:
Constant feed rate:
Center-to-center spacing:
, then
Tolerance time is the time a work unit spends in a workstation:
Total elapsed time is the time a work unit spends on the line:
Chapter 5 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
17