## Slide 1: Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 1
Introduction to Work Measurement
1

## Slide 2: Introduction to Industrial Engineering
Industrial engineering focuses on optimizing complex processes or systems by improving efficiency and effectiveness while ensuring quality and productivity.
Involves:
People: Workforce management
Machines: Automation and machinery
Materials: Efficient material usage
Information: Data management
Energy: Sustainable energy use
Nature of work include:
        Process Design: Developing efficient workflows
        Systems Analysis: Studying system components
        Operations Management: Managing day-to-day operations
        Quality Control: Ensuring products meet standards
        Ergonomics: Designing for human efficiency and comfort
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Historical Context and Principles
Industrial Revolution:
Began in Great Britain around 1770
Shift from small workshops to large factories
Introduction of machinery increased production capacity
Centralization of production under one roof
Minimum Wage Laws:
Emerged due to worker exploitation (extremely low pay, long hours and poor working conditions)
First laws enacted in Australia and New Zealand (late 19th - early 20th centuries)
New Zealand's Industrial Conciliation and Arbitration Act of 1894 and Australia's New South Wales Minimum Wage Act of 1907 set the precedent
Fair Labor Standards Act of 1938: established the first federal minimum wage in the U.S
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Labor Specialization and Efficiency
Adam Smith: "Wealth of Nations" (published in 1776)
Discussed labor specialization
Emphasized efficiency gains from dividing labor into specific tasks
Henry Ford: Assembly line
Revolutionized automobile production
Each worker performs a specific task
Reduced production time and costs
Made cars affordable for the masses
Factories:
Centralized production allowed for greater control
Urbanization: People moved from rural areas to cities for work
Led to worker movements and the rise of labor unions
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Key Historical Figures
Eli Whitney: Invented the cotton gin and popularized interchangeable parts
Henri Fayol: Developed the line and staff organization model
Henry Ford: Introduced the moving assembly line
Frederick Winslow Taylor: Father of scientific management
Frank and Lillian Gilbreth: Pioneers in motion study and efficiency
Harold B. Maynard: Developed Methods-Time Measurement (MTM)
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Eli Whitney (1765-1825)
Invention: Cotton gin
Revolutionized cotton processing
Contribution:
Concept of interchangeable parts
Allowed for mass production and easier assembly/repair
Special machine tools, fixtures, and gauges for accurate components
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Henri Fayol (1841-1925)
Model: Line and staff organization
Line roles: Direct activities (production, sales)
Staff roles: Specialized support (HR, legal, accounting)
Emphasis: Planning in management
Assess future and make provisions
Improved organizational efficiency and accountability
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Henry Ford (1863-1947)
Innovation: Assembly line
Moving assembly line reduced production time and costs
Impact:
Model T: First affordable car
Mass production techniques
Increased efficiency in the automobile industry
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Frederick Winslow Taylor (1856-1915)
Known as: Father of scientific management. Published book in 1911
Taylor’s Four Principles:
Develop a science for each element of work
Scientifically select, train & develop workers
Cooperate with workers
Divide Work and Responsibility
Two Famous Experiments:
Shoveling experiment: Optimal load size for efficiency
Pig iron handling: Improved efficiency with specific methods and rest breaks
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Frank and Lillian Gilbreth
Frank Gilbreth (1868-1924):
Known as “Father of motion study”
Developed two theories:
    Therbligs: 17 basic motion elements
  Principle of "one best way" to perform tasks
Lillian Gilbreth (1878-1972):
Integrated psychology with scientific management
Developed industrial and organizational psychology
Continued their work after Frank’s death
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Harold B. Maynard (1902-1975)
One of the most important figures in development of predetermined motion time systems.
Development: Methods-Time Measurement (MTM) system
MTM: Database of motion elements for time standards
  Became most successful & widely used first-level PMTS
MOST: Maynard Operation Sequence Technique
  Introduced in Sweden in 1972 and U.S. in 1974. One of the most widely used PMT systems
Contribution:
Improved efficiency in industrial settings
Developed several MTM systems for specific work situations
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11

## Slide 12: Importance of Time & Methods to Determine Time Standards
Impact:
Productivity: Determines output rate
Costs: Affects labor and production costs
Efficiency: Measures effectiveness of processes
Estimation:
    Expert consultation
    Least reliable method
Historical Records:
  Documentation of previous production runs
  Improvement over estimation
    Work Measurement Techniques:
Direct Time Study
Predetermined Motion Time Systems (PMTS)
Standard Data Systems
Work Sampling
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
12

## Slide 13: Work Measurement Techniques
Direct Time Study:
Observes and times work elements
Uses timing devices like a stopwatch
Performance rating assigned by time study analyst
Predetermined Motion Time Systems (PMTS)
Uses predetermined motion times
Normal times for basic motion elements
No need for performance ratings
Standard Data Systems:
Uses normal time values from various sources
Compiles a database for calculating time standards
Allows pre-production time estimation
Work Sampling:
Uses random observations
Studies work situations to determine time proportions
Less precise than direct time study
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
13

## Slide 14: Requirements for Valid Time Standards
Must be:
Accurate: Precise and reliable
Consistent: Applicable across different workers and conditions
Fair: Attainable by a trained worker under normal working conditions
To accurately determine standard time for a task:
Task must be performed by an average worker.
Worker’s pace represents standard performance.
Worker follows a standard method.
Task is performed on a standard work unit that is defined pre- and post-processing.
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
14

## Slide 15: Relative Accuracy of Time Study Methods
Least Accurate: Estimation
Relies on estimator’s judgment
Not based on actual data
Historical Records: Improvement over estimation
Uses hard data from previous production runs
May have biases or missing data
Work Sampling: Least accurate among the work measurement techniques
Statistical errors from sampling process
Does not capture methods variation
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
15

## Slide 16: Productivity in Work Systems
Productivity is an important metric in work systems and is defined as the ratio of outputs to inputs of a given production or service process. 4
Labor Productivity Index:
  Measures productivity changes over time
  LPR = labor productivity ratio, WU = no. of work units of output, and LH = labor hours of input
  LPI = labor productivity index, LPRt = labor productivity ratio for a future time period, and LPRb = labor productivity ratio for the baseline period
Chapter 1 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
16