## Slide 1: Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 6
Motion Economy
and Work Design
1

## Slide 2: Introduction
Motion economy and work design are crucial for enhancing productivity, reducing worker fatigue, and improving efficiency.
Focus areas include:
fundamental motion elements
work analysis techniques
human body principles
workplace arrangement
tooling and equipment design
SIMO chart
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Purpose and Advantages of Motion Economy
Purpose:
Enhance productivity
Reduce fatigue
Improve safety
Standardize work
Optimize resource use
Advantages:
Increased efficiency
Cost reduction
Enhanced worker morale
Quality improvement
Better ergonomics
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Basic Motion Elements and Work Analysis
Any manual task is comprised of work elements which can be decomposed into basic motion elements.
Gilbreth's 17 Therbligs: Frank and Lillian Gilbreth developed Therbligs, a system to categorize basic motion elements, with the name being a play on "Gilbreth" spelled backwards. Therbligs represent fundamental units of work, each denoting a specific action performed by workers. Analyzing these elements helps identify inefficiencies and improve work design.
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Principles of Motion Economy
Developed over decades of practical work, the principles of motion economy aim to maximize worker efficiency and minimize fatigue by analyzing work methods, workplace layout, and the tools and equipment used.
Categories of principles:
Principles related to the human body
Principles related to workplace arrangement
Principles related to the design of tooling and equipment
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Principles Related to the Human Body
Motion economy principles should consider the most appropriate methods and motions for human workers performing tasks.
Use of both hands
Minimize fatigue
Use gravity whenever possible
Natural movements
Proper height and reach
Preferred hand usage
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Principles Related to Workplace Arrangement
Motion economy principles should focus on workplace design, particularly the workstation layout and the arrangement of tools and parts.
Fixed locations for tools and materials
Minimize motions
Accessibility
Comfortable environment
Gravity feed bins or drop chutes
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Normal and Maximum Working Areas
Normal and Maximum Working Areas are key concepts in methods and motion study, used to design efficient and ergonomic workspaces. These areas define optimal zones for comfortable and strain-free tool and material operation.
Normal Working Area: The zone where a worker can comfortably perform tasks with minimal arm and body movement, typically involving forearm motions while keeping the upper arm relatively still.
Maximum Working Area: Extends beyond the normal area, involving full arm extension and body movement, which can increase fatigue and reduce efficiency if used frequently.
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Dimensions of Normal and Maximum Working Areas
Dimensions vary based on ergonomic standards and workplace requirements but follow general guidelines.
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Example: Assembly Workstation Design
Designing workspaces with these principles enhances efficiency & reduces fatigue, minimizing unnecessary movements for safer and more productive work environments.
Normal Working Area:
Place essential tools (screwdrivers, pliers, small parts) within easy reach.
Arrange immediate assembly components in this zone.
Use an ergonomically designed chair when feasible.
Maximum Working Area:
Store large components and infrequently used tools outside the normal area but within reach.
Ensure items require minimal movement to access and are not needed constantly.
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Example: Office Work Area
Properly defining these areas enhances ergonomics, efficiency, and reduces worker fatigue, leading to more comfortable and productive workstations.
Normal Working Area:
Place keyboard, mouse, frequently used documents, and small supplies (pens, notepads) within easy reach.
This area covers the immediate desk space in front of the worker.
Maximum Working Area:
Store less frequently used items (telephone, reference books, personal items) in the peripheral desk space and nearby shelves or drawers.
Items should be accessible with minimal effort but not interfere with primary tasks
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11

## Slide 12: Good vs. Bad Workplace Arrangements
 | Good | Bad
Principles | Follow motion economy principles Minimize unnecessary movements Reduce worker fatigue | Ignores motion economy principles Leads to inefficiency, fatigue, and injury risk
Features | Tools and materials within easy reach (30-40 cm from shoulder) Clear, clutter-free workspace Proper lighting and ergonomic design | Tools and materials out of reach Cluttered workspace Poor lighting and ergonomics
Key Elements | Frequently used tools (e.g., screwdriver) in normal working area Infrequently used tools (e.g., hammer) in maximum working area Organized work surface Adequate lighting Ergonomic chair and workstation | Frequently used tools far from worker Mixed tool organization causing confusion Cluttered work surface Inadequate lighting Non-ergonomic chair and workstation
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
12

## Slide 13: Principles Related to the Design of Tooling and Equipment
Motion economy principles should consider the design of special tools and equipment controls used in the workplace.
Ergonomic tools
Standardization
Workholder devices
Multi-purpose tools
Use of foot or knee devices
Automation
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
13

## Slide 14: Work Analysis with SIMO Chart
SIMO (Simultaneous Motion) Chart analyzes and documents simultaneous movements of a worker’s hands during a task. It identifies inefficiencies and idle time to optimize productivity and reduce fatigue.
Steps to Create a SIMO Chart:
Observe and record each motion of both hands.
Classify motions using Therbligs.
Construct a two-column chart for left and right hands with a time scale.
Analyze for idle or non-value-added motions.
Optimize to synchronize movements and balance workload.
Example: Assembly of a Small Electrical Component
Analysis:
Chart shows idle periods for the left hand, indicating inefficiencies.
Introducing parallel actions can reduce idle time and improve efficiency.
Chapter 6 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
14