## Slide 1: Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 9
Direct Time Study
1

## Slide 2: Introduction
Direct Time Study: Observation and timing of tasks by a trained analyst at a job site.
Purpose: Establish accurate and fair time standards for planning, scheduling, and productivity improvement.
Key Points:
Suitable for manual tasks that can be physically observed.
Ideal for repetitive tasks, typically done in 15 minutes or less.
Applicable to tasks repeated in a cyclical pattern over an extended period.
Most versatile and widely used work measurement technique.
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Steps in Direct Time Study
Select Task
  Identify the specific task to study.
Define Work Elements
  Break task into distinct steps.
Record Observations
  Measure time for each element using a stopwatch.
Evaluate Performance
  Assess worker’s pace against a standard.
Calculate Normal Time
  Adjust observed times based on performance ratings.
Determine Allowances
  Add time for fatigue, personal needs, and delays.
Calculate Standard Time
  Combine normal time and allowances for the final standard time.
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Definitions
Time Study Record: Data collection form that contains necessary info to compute task duration.
Column Number: Top number of each column on the form.
Sample Size: Minimum observations for statistical accuracy.
Element Description: Brief description of a task step.
Element Times: Stopwatch times for each task repetition.
Total Time: Sum of times for an element.
Number: Observations excluding foreign elements.
Foreign Element: Unusual work conditions noted separately.
Average Time: Total time divided by number of observations.
Rating Factor: Employee's performance relative to normal speed.
Base Time: Average time multiplied by rating factor.
Frequency: How often an element occurs.
Normal Time: Base time adjusted by frequency.
P,F, and D: Allowances for personal needs, fatigue, and delays.
Total Standard Time: Sum of time for average trained employee at normal pace.
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Time Study Equipment
Tools:
Stopwatch: Calibrated in 1/1000 of a minute or seconds.
Time Study Record Forms: Data collection sheets.
Basic Supplies: Clipboard, pencil, and tape measure.
Additional Tools: Tachometer or gauge for machine speeds, feed rates, and other critical parameters.
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Snapback Time Study
Procedure
Start Stopwatch: Begin at the first element.
Snapback to Zero: After each element, read and reset the stopwatch.
Record Time: Log the elapsed time for each element on the form.
Common Issue
Timing Errors: Snapping the watch too early or late affects element times but not total time.
End of Study
Total Elapsed Time: Read and record at the bottom of the form.
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Continuous Time Study
Process: Stopwatch is started at the beginning of the first cycle and runs without stopping.
Recording: Analyst notes the elapsed time at the end of each element.
Adaptation: Some analysts reset the stopwatch at the start of each work cycle to always begin from zero.
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: General Time Study Procedure – Part 1
Select Job:
Based on requests (employee, supervisor, management) or audits/projects.
            Discuss and Introduce:
Talk with the section supervisor.
Introduce yourself to the employee and explain the study.
      Verify Method:
Ensure the employee follows the standard method.
Record Details:
Note equipment, speeds, tools, materials, etc.
Sketch the work area if needed.
Observe and Divide:
Break job into logical elements.
Record Time:
Watch and note the time for each element.
Rate Elements:
Evaluate each element individually.
Collect Data:
Gather data over several complete cycles.
Compute Times:
Calculate base and normal times.
Add allowances to determine standard time.
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: General Time Study Procedure – Part 2
Post-Time Study Actions:
Determine Observation Cycles: Based on desired confidence level.
Continue Timing: Observe enough cycles.
Compute Standard Time: Derive engineered standard time from all studies.
Evaluate Productivity: Assess employee productivity.
Approve and Publish: Get approval and release the new standard time.
File Documentation: Store all materials for future reference.
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: How to Collect Time Study Data
Prepare Recording Device:
Use a camcorder, smartphone, iPad, etc
Observe Task:
Familiarize yourself with work elements and normal worker pace
Record Task:
Video the entire process
Break Down Video:
Separate into distinct work elements
Record Times:
Note work element times on the worksheet
Timing Elements:
Long elements: Time individually
Short elements: Time in groups
Foreign Elements:
Code and compute these at the end of the study
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Time Study Equipment
Direct Time Study
Observation Tools: Stopwatch, video camera, or computerized methods
Stopwatch Time Study
Traditional Tools: Stopwatch and worksheet on a clipboard
Measurement Scales: Decimal minutes, decimal hours, TMUs (1 TMU = 0.036 seconds)
Digital Stopwatches: Digital display, easy readability, reduced reading errors, switching between time scales
Video Recorded Time Study
Devices: Camcorder, iPad, smartphone
Advantages: Captures visual and audio elements, allows detailed analysis by advancing/reversing video, provides objective assessment and record of task
Computerized Time Study
Systems: PMTS, SDS
Goals: Set time standards and describe task methods, maintain a database of empirical time standards
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11

## Slide 12: Accuracy of the Standard Time
Importance of Documenting Standard Methods
Identify Method Changes: Justify retiming tasks
Work Instructions: Guide for future batches
Reference Document: Resolve disputes between management and workers
Data for Standard Systems: Future use in standard data systems
Key Influencing Factors
Employee Efficiency:
  Analyst's ability to rate performance accurately
Study Conditions:
  Equipment performance
  Raw material quality
  Employee fatigue
Job Division:
    How job is broken into elements
Number of Cycles:
  Sufficient observation cycles
Statistical Methods:
  Use Student t-distribution for small sample sizes
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
12

## Slide 13: Irregular & Foreign Elements
    Irregular Elements: Performed less than once per cycle
    Examples: Changing tools, replacing tote pans
    Foreign Elements: Unusual elements during a normal work cycle
    Examples:
    F: Fumble
    P: Personal movement
    M: Minor adjustment
    R: Repair/rework
    S: Replenishing supplies
    Computing Foreign Elements
    Note: Mark unusual element on the form
    Average Time: Calculate average time excluding foreign element
    Adjust Time: Subtract average element time from foreign element time
    Base Time: Multiply by rating factor
    Frequency Adjustment: Adjust by occurrence frequency for normal time per cycle
    Omitting an Element
    Paid Elsewhere: Included in another standard part
    Irrelevant: Does not belong in the standard
    Outlier: Time outside normal range without clear cause
Chapter 9 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
13