## Slide 1: Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 4
Workflow and Yield
1

## Slide 2: Introduction
Production and delivery processes require multiple operations
Operations may be sequential or simultaneous
Movement of work units across workstations
Batch processing as a practical approach
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Sequential Operations and Workflow
Sequential operations involve performing tasks consecutively in a specified sequence. Completion of one task before the next. Work units can be materials, parts, products, or people.
Precedence constraints are machine or processing limitations that dictate the order of operations, ensuring that certain tasks are completed before others can commence.
                Examples:
              Drilling a hole before tapping threads
              Airport security check before boarding
              Anesthetized before dental procedures
Workflow involves the physical movement of materials and work units, along with an information flow that monitors and controls this movement, governed by the production schedule and job tickets.
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Workflow Patterns (Part 1)
Types:
Pure Sequential Pattern: all work units follow the same sequence of operations without variation
Mixed Sequential Pattern: different work units follow varied sequences through different workstations.
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Workflow Patterns (Part 2)
Four Types of Movements:
Linear flow: A work unit moves directly to the next operation downstream, without reversing.
Bypassing: A work unit skips adjacent workstations and moves to a further one downstream.
Backflow: A work unit moves backward to a previous workstation.
Repeat operation: An operation is repeated at the same workstation, either due to multiple attempts or the need for different setups.
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Bottlenecks in Sequential Operations
Bottleneck restricts flow, slowing the entire system. Upstream operations must match the bottleneck's rate to avoid restrictions.
Concepts:
Blocking: Upstream operations are halted when limited by downstream bottlenecks. Downstream operations can't exceed the bottleneck's rate.
    Example: A full storage area stops the production line.
Starving: Downstream operations lack work, limited by upstream bottlenecks.
Example: A machine waits for raw materials from the forklift operator.
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Causes of Bottlenecks and Solutions
Causes:
Equipment breakdowns
Variability in processing times
Limited capacity
Solutions:
Adding capacity or resources
Improving maintenance and reliability
Balancing workloads
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Batch Processing
Batch processing is when items are processed in batches, not individually. Applies to materials, products, information, or people. Common in production, logistics, and services.
Examples:
Producing identical parts
Airplane passengers traveling
Washing laundry
Two Types:
Sequential batch processing: batches processed one after another.
Simultaneous batch processing: multiple batches processed simultaneously on different resources.
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Pros of Batch Processing
Economies of Scale:
Reduced cost per unit
Work Unit Differences:
Accommodating changes in production methods (also known as “setups”)
Machine/Equipment Limitations:
Restrictions on size, weight, or quantity
Material Limitations:
Division into sub-units (also known as “multiple-out”)
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9

## Slide 10: Cons of Batch Processing
Interruptions:
Discontinuity between batches due to setups or changeovers
Lead Times and WIP Inventory:
Build-up of batches
Long lead times and work-in-process inventory
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
10

## Slide 11: Economic Order Quantity Model
Model of Inventory Level:
Gradual withdrawal and replenishment
Maximum inventory level determined by order quantity
Equations:
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
11

## Slide 12: Economic Order Quantity Example
Example Problem:
The annual demand for a made-to-stock item is 2,000 units at $10 each, with a holding cost rate of 15% per year. Setup time is 1.5 hours at a cost of $150 per hour. Determine the Economic Order Quantity (EOQ) and total inventory cost.
Determine the Economic Order Quantity (EOQ) and the total inventory cost for this case.
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
12

## Slide 13: Workload and Available Time
Workload as the sum of work units multiplied by cycle time.
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
13

## Slide 14: Worker and Machine Requirements Example
Example Problem:
To meet future production requirements in the engine lathe department, new machines and operators must be acquired. The department will produce three new parts: Part A (25,000 units/year at 6.2 min/unit), Part B (30,000 units/year at 3.4 min/unit), and Part C (41,000 units/year at 7.6 min/unit). Operations will run one 8-hour shift for 250 days/year. Machines are expected to be 97.8% reliable, with an anticipated scrap rate of 3.2%, and worker efficiency at 100%.
How many new engine lathes and operators are required to meet these production requirements?
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
14

## Slide 15: Fraction Defect Rates
Fraction defect rates is the impact of defect rates on final quantity.
Equation:
Input/output relationship in unit operations
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
15

## Slide 16: Fraction Defect Rates: Example 1
Scenario: Multiple Processes with Same Fraction Defect Rates
A batch of 7,000 units undergoes 5 sequential operations, each with a 2% defect rate.
Determine (a) the number of good parts, (b) defects in the final batch, and (c) the yield of the operation sequence.
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
16

## Slide 17: Fraction Defect Rates: Example 2
Scenario: Multiple Processes with Different Fraction Defect Rates
A batch of 20,000 parts undergoes 4 operations with defect rates of 2% for operations 1 and 2, 3% for operation 3, and 6% for operation 4.
Determine (a) the number of good parts, (b) defects in the final batch, and (c) the yield of the sequence.
Chapter 4 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
17