## Slide 1: Chapter 13 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
Chapter 13
Work Sampling
1

## Slide 2: Introduction
Definition: Work sampling is a statistical technique used to estimate the proportion of time spent on various activities in a workplace.
Method: Involves random observations over time to determine how work is distributed among tasks, suitable for both repetitive and non-repetitive tasks.
Example: A janitor's tasks (e.g., mopping, vacuuming) are observed randomly; the time spent on each task is estimated from these observations.
Chapter 13 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
2

## Slide 3: Major Uses of Work Sampling
Measuring Work Performance: Estimate the time employees spend on productive vs. non-productive tasks.
Determining Utilization Rates: Assess machinery and equipment usage.
Setting Standards: Develop performance standards based on observed data.
Analyzing Work Distribution: Identify bottlenecks and workload imbalances.
Delay Studies: Determine the percentage of the day when employees aren't doing their assigned jobs.
Chapter 13 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
3

## Slide 4: Work Sampling Procedure
Define Purpose and Scope: Identify activities to study and set the time period.
Design the Study: Determine sample size and develop a sampling plan.
Collect Data: Conduct random observations and record activities.
Analyze Data: Categorize and calculate the proportion of time spent on each activity.
Interpret Results: Identify patterns, inefficiencies, and recommend improvements.
Chapter 13 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
4

## Slide 5: Examples of Work Sampling Applications
Manufacturing: Evaluate machine utilization, operator efficiency, and downtime causes.
Service Industries: Assess efficiency in healthcare, hospitality, and retail.
Administrative Work: Identify non-value-added tasks and streamline processes.
Healthcare Facility: Analyze nurse time allocation between patient care and other duties.
Retail Store: Observe how sales associates spend time assisting customers, restocking, and cashiering.
Chapter 13 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
5

## Slide 6: Advantages of Work Sampling
Cost-Effective: Requires fewer resources and less time.
Minimal Disruption: Observations are random, causing less interference.
Broad Scope: Suitable for various industries and non-repetitive jobs.
Flexibility: Can be performed over long periods, detecting a range of variables.
Chapter 13 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
6

## Slide 7: Disadvantages of Work Sampling
  Statistical Variability: Accuracy depends on the number of observations.
  Potential Bias: Workers may alter behavior if aware of being observed.
  Limited Detail: Provides an overview rather than in-depth insights.
  Data Interpretation: Requires careful analysis of statistical principles.
Chapter 13 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
7

## Slide 8: Determining Minimum Sample Size
Sample Size (n): Dependent on:
Z-Value: Based on alpha (∝), the chance of being wrong.
Variability: Estimate of the process variability (standard deviation or sample proportion).
Acceptable Error (e): The range within which we are comfortable with the answer.
Equations:
Variable Data:
Attribute Data:
Chapter 13 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
8

## Slide 9: Confidence Interval (CI)
CI for Variable Data:
Example: 95% CI for a mean length of 50 mm with a standard deviation of 2 mm in a sample of 30 parts is between 49.284 mm and 50.716 mm.
Formula:
CI for Attribute Data:
Example: 95% CI for a sample of 200 products with 30 defects is between 10.05% and 19.95% defective.
Formula:
Chapter 13 Copyright © 2025 by Robert S. Keyser, Parisa Pooyan, Lin Li, & Suad Awad - All Rights Reserved
9